Systems Integration
with Free Software
- dhcp -
    Xavier Castaño García

---
This session
We are going to talk about:
  - DHCP protocol
  - DHCP client
  - DHCP server

---
Introduction to DHCP(I)
Dynamic Host Configuration Protocol
DHCP is a protocol used by Networked devices to obtain several parameters necessary for the clients.
DHCP can be used to automatically assign IP addresses, to deliver TCP/IP stack configuration parameters such as the subnet mask and default router, and to provide other configuration information such as the addresses for printer, time and news servers.

---
Introduction to DHCP(I)
DHCP is based in an architecture “Client-Server” where:
  - Client asks for information
  - Server answers with the information it has.
DHCP works in port 67/UDP for the server side and 68/UDP for the client side.

---
Introduction to DHCP (II)
DHCP has different methods for IP addresses allocation:
  - dynamic_allocation: A network manager assigns a range of IP to DHCP.
  - automatic_allocation: The DHCP server permanently assigns a free IP address to a requesting client from the range defined by the administrator.
  - manual_allocation: The DHCP server allocates an IP address based on a table with MAC address.

---
Introduction to DHCP (III)
DHCP has several messages:
  - DHCP discovery: The client multicasts on the physical subnet to find available servers.
  - DHCP offers: When a DHCP server receives an IP lease request from a client, it extends an IP lease offer.
  - DHCP requests: The client accepts the offer.
  - DHCP acknowledgement: Final phase.

---
Introduction to DHCP (III)
Typical sequence diagram:

---
Introduction to DHCP (III)
Other messages:
  - DHCP release: The client releases the IP.
  - DHCP information: Requests more information than the server sent with the original DHCPACK
RFC:
  - ftp://ftp.isi.edu/in-notes/rfc2131.txt

---
DHCP server (I)
DHCP server is installed from this packages:
  - dhcp3-server in Ubuntu
  - dhcp in Debian
After installing the package we need to configure some things:
  - You should test “ifconfig -a” to view if “MULTICAST” is enable in the interface.
  - You should add the route 255.255.255.255:
    - route add -host 255.255.255.255 dev eth0

---
DHCP server (II)
Configuring dhcpd.conf:
  - “option”: you can define common options for all supported networks. For example:
    - option domain-name “mswl.com”
    - option domain-name-servers ns1.mswl.com ns2.mswl.com
  - “authoritative”: Example of use, your laptop has a old IP (from one subnet) from your home and you are at the office (other subnet). If you want to force to forget the old IP you need this configured.
  - subnet: directive for defining subnet configuration.

---
DHCP server (III)
Configuring dhcpd.conf:
  - shared-network: directory for defining IP subnets that actually share the same physical network.
  - host: There must be at least one host statement for every BOOTP client that is to be served.
  - group: The group statement is used simply to apply one or more parameters to a group of declarations.

---
DHCP server (III)
First example, assigning IP addresses randomly:
    - option subnet-mask 255.255.255.0; #Its subnet mask
    - option broadcast-address 192.168.1.255; #Client should use this IP as Broadcast.
    - option routers 192.168.1.254; #Is the router/gateway
    - option domain-name-servers 192.168.1.1, 192.168.1.2; #Its DNS servers
    - option domain-name "mswl.com";
    - subnet 192.168.1.0 netmask 255.255.255.0 {
    - range 192.168.1.10 192.168.1.100; # One of this range will be offered
    - range 192.168.1.150 192.168.1.200; # Or one of this range will be offered
    - }

---
DHCP server (III)
Second, assigning fixed IP addresses to known hosts:
    - default-lease-time 6000; # It will lease an IP address for 600 seconds if the client doesn't # ask for specific time frame
    - max-lease-time 7200; # The maximum (allowed) lease will be 7200 seconds
    - subnet 192.168.1.0 netmask 255.255.255.0 { #Declares a subnet...
    - option domain-name "mswl.com";
    - option domain-name-servers 192.168.1.1, 192.168.1.2; #Its DNS servers
    - option routers 192.168.1.3;
    - host myhostname {
    - hardware ethernet 00:00:00:00:00:00; # MAC address for host
    - fixed-address 192.168.1.4; # This IP will be assigned to myhostname.
    - }
    - }

---
DHCP server (III)
With the server configured:
  - The file “dhcpd.leases” should be created if doesn't exists.
        - touch /var/lib/dhcp3/dhcpd.leases ## In Ubuntu this file exists...
  - You can now start the server:
    - /etc/init.d/dhcp3-server restart
  - See more info:
    - http://www.isc.org/index.pl?/sw/dhcp/dhcpv3-README.php
    - http://tldp.org/HOWTO/DHCP/index.html
    - http://www.arda.homeunix.net/dnssetup.html

---
DHCP client (I)
DHCP needs configuration of server and client.
DHCP client in Ubuntu:
    - apt-get install dhcp3-client dhcp3-common
The dhcpcd package installs it's startup script as usual for debian packages in /etc/init.d/package_name, here as /etc/init.d/dhcpcd, and links this to the various /etc/rcX.d/ directories.

---
DHCP client (II)
In order to configure one interface (for example, eth0) with dhcp you need to add to “/etc/network/interfaces” this line:
  - auto: the interface should be configured during boot time.
  - inet: interface uses TCP/IP networking.
  - dhcp: the interface can be configured through DHCP.
auto eth0
iface eth0 inet dhcp

---
DHCP client (III)
If you don't want to use DHCP you could add static configuration:
      - iface eth0 inet static
      - address 192.168.12.2
      - netmask 255.255.255.0
      - gateway 192.168.12.254

---
DHCP client (IV)
A view to dhclient.conf:
  - retry: Time to determine if there isn't server.
  - reboot: dhcp first tries to reacquire the last address it had, this is the time to try to reacquire the old IP.
  - request: Options that the client requests to receive in an offer.
  - require: Options that the client requires to accept an offer.
  - send: Client send the specified options.
  - lease: For alternate database after timing.

---
DHCP client (V)
The options are in “man dhcp-options”. Some of them:
  - option subnet-mask: Clients subnet mask.
  - option routers: Router on the client subnet.
  - option domain-name-servers: List of domain name servers.
  - option domain-name: Domain name that client should use when resolving hostnames via the Domain Name System.

---
DHCP client (V)
Example of configuration:
      - timeout 60; # time between begins and the time that it decides that it's not going
      - # to contact with the server
      - retry 60;
      - reboot 10; # Seconds to maintain old IP in a reboot.
      - select-timeout 5; # select-timeout has expired, the client will accept the first offer
      - reject X.X.X.X; #Rejects offers from this IP as server.
      - alias { #While roaming forcing that the client has an alias with fixed IP.
      - interface "eth0";
      - fixed-address 192.5.5.213;
      - option subnet-mask 255.255.255.255;
      - }

---
DHCP client (V)
Continuation of example:
      - lease {
      - interface "eth0";
      - fixed-address 192.33.137.200; #Old IP given by below router
      - medium "link0 link1"; #Type of network to connect.
      - option host-name "MyHostnameOnNetwork"; #Host name
      - option subnet-mask 255.255.255.0; # Subnet mask
      - option broadcast-address 192.33.137.255;
      - option routers 192.33.137.250; #Router with it will try to contact to bind with IP
      - option domain-name-servers 127.0.0.1;
      - renew 2 2008/4/12 00:00:01; #Time to try to contact with its server.
      - rebind 2 2008/4/12 00:00:01; #Time to try to contact with any server.
      - expire 2 2008/4/12 00:00:01; # Client must stop using a lease if it has not been
                - # able to contact a server in order to renew it.
      - }

---
Appendix A: Firewalls
Firewalls usually have to permit DHCP traffic explicitly. Anti-spoofing policy rules and tight inclusive firewalls often stop such packets.
  - To allow DHCP, network administrators need to allow several types of packets through the server-side firewall.
    - Incoming packets from 0.0.0.0 or dhcp-pool to dhcp-ip.
    - Incoming packets from any address to 255.255.255.255
    - Outgoing packets from dhcp-ip to dhcp-pool or 255.255.255.255